## Slide 1
Unconventional Enhanced Oil Recovery (EOR)
H. Kazemi, Professor
Colorado School of Mines
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
1
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 2
Wet Gas Injection is the EOR King in Unconventional Reservoirs (1)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Wet gas injection penetrate micro and macro fractures. Then, interface and interphase molecular mixing (diffusion) enhances production.
Low salinity water if forced to enter micro and macro fractures, then, osmotic interface mass transport pushes the oil out of the matrix. The oil and water in the micro and macro fractures are immiscible; thus, causing very low mobility, immiscible two-phase or three-phase environment. If we break the IFT, the oil in the fractures can be potentially produced effectively. This is the current area of our research in the PE department.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 3
Basic Premise of Non-Gas EOR in Unconventional Reservoirs (2)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Displace oil out of the nanopores to micro ad macro fractures. The key word is displacement.
Displacement requires pressure gradient—leading to advective flow. Simple calculation shows that this is very impractical (Next Slide)! Just imagine a pore throat of 100 nanometer diameter. Its permeability is less than 10 micro Darcy. Such a pore channel requires a very large pressure gradient to generate realistic displacement velocities.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 4
Hydraulic Fractures Placed in One Square Mile Compared with Equivalent Vertical Wells
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
320 fraced vertical wells in
one square mile
11 zipper fraced horizontal
wells in one square mile
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 5
Centrifuge Measurements in A Bakken Core, Indicating a Very Narrow Mobile Saturation Range (Somayeh Karimi, CSM, 2015)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Mobile saturation window to WF ~ 10 %
Mobile saturation window to GF ~ 30 %
Residual oil saturation to water ~ 29.7%
Irreducible water saturation
~ 62%
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 6
Basic Premise of Non-Gas EOR in Unconventional Reservoirs (3)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
As an alternative, let us examine the micro and macro fracture channels surrounding the matrix pore assemblage. Displacement in these fractures is more realistic because tortuosity is much smaller.
In this scenario, an appropriate EOR fluid (such as low-salinity brine) can enter the matrix by chemical osmosis forcing the oil to be displaced into the micro and macro fractures. Thus, the fractures will be in two- or three-phase flow condition. If we can break the IFT in these fractures, we can produce the displaced oil.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 7
Basic Premise of Non-Gas EOR in Unconventional Reservoirs (4)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
To reduce IFT, one can use a low concentration of an appropriate non-ionic surfactants in carbonate shale reservoirs.
Other possibilities include the use of nanoparticle colloidal dispersions.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 8
Acidic crudes potentially render carbonates oleophilic
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Carbonate rock surface is believed to be positively charged (+) either because of calcium atom residing near the surface of calcite crystal, or presence of Ca++ precipitate on the calcite surface resulting from calcite dissolution in water. Because of this positive charge, crude’s carboxylate ions (-) become attracted to the carbonate pore surface, rendering it oleophilic:
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 9
Oil expulsion by brine imbibition and gravity segregation in an 82-mD, sucrosic carbonate core after 6 days of exposure (Yates Field, USA)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 10
Carbonate dissolution in low-salinity water
may promote EOR
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Altahir and Hussain (2017) experimental results indicate that a pH of about 9.5 is generated because of calcite dissolution in low salinity water. This alkaline environment could be the driving mechanism for low-salinity EOR probably by OH- bonding illustrated below and on the following slide.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 11
Acidic crude possible interaction with calcite (Adopted from: Austad et al., 2010)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 12
Sea water potentially alters carbonates from oleophylic to hydrophilic (Adopted from: Austad et al., 2010)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 13
Eleven Wells in the One Square Mile Study Area And a Well Path (Yanrui Ning, CSM, 2017)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Pitcher, 2015
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 14
Significant Interwell & Interlayer Communication
(Yanrui Ning, CSM, 2017)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 15
Conclusions
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Displacement-based EOR is impractical in unconventional reservoirs.
Micro and macro fractures are the key flow paths for getting the primary and EOR oil out.
While gas injection EOR is the king of oil recovery in unconventional shale reservoirs, low-salinity osmosis, plus an IFT reducer, can lead to additional oil production. This is the current state of our research at CSM.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 16
Questions?
Thank you
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado