## Slide 1
MODELING OF TRANSIENT FLOW OF DIAGNOSTIC FRACTURE INJECTION TESTS IN POROUS MEDIA
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Mohamed Ibrahim Mohamed
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 2
Only a few analytical studies focus on the effect of randomly distributed natural fractures on the pressure transient during falloff.
However, most of the studies have focused on the geomechanics approach of the minifrac analysis and the pressure transient solutions have been overlooked.
Understand the complete picture of the pressure transient responses in the natural fractures as well as the main fracture.
Unfortunately, many field tests that are done provide misleading results because of either incorrect analysis of the acquired data or problematic data acquisition.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Motivation
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 3
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Objectives of Study
  First develop a geomechanics coupled reservoir flow simulation for Minifrac tests.
  Allow modeling of pressure response of minifrac before and after fracture closure.
  Second develop semi-analytical model that simulates transient flow in a porous media, which contains finite conductivity, randomly connected and disconnected, fractures.
    Investigate the properties of main fracture as well as natural fractures, such as length, azimuth, conductivity and fracture distribution on the pressure during falloff.
  Third discuss specific issues that result in poor estimation of reservoir properties.
    Apply machine learning methods to predict the fracture closure pressure
    Minimize shortcomings in determining for non-ideal or subjective conditions.
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 4
Geomechanics Coupled Reservoir Flow Simulation
Numerical Simulation (SPE-199728-MS)
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 5
GEM is used in the study
Describes relationship between the permeability of the fracture system and fracture opening.
As pressure increases in regular grid, the normal effective stresses on the fractures decrease.
Stress breaks past the failure envelope of the rock  fracture propagates and allow fluid to flow through the fracture system in addition to the underlying matrix system.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Geomechanics Coupled Reservoir Flow Simulation
Barton-Bandis stress permeability relationship model
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 6
Barton-Bandis parameters used in this test case were obtained by history matching a field case.
The history matching was done by using
  Actual field injection schedule
  Bottom hole pressure recorded using a downhole gauge
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Geomechanics Coupled Reservoir Flow Simulation
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Initial Fracture Aperture (ft) | 1.4E-05
Fracture Stiffness (psi/ft) | 536000
Fracture Opening Stress (psi) | 6750.4
Hydraulic Fracture Permeability (mD) | 134.4
Fracture Closure Permeability (mD) | 63.6
Fracture Residual Permeability (mD) | 9.6
Barton-Bandis parameters for test case.

## Slide 7
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Geomechanics Coupled Reservoir Flow Simulation
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Pressure Response Interpretation:
Breakdown pressure
  Relatively higher than the breakdown pressure observed from the field data.
G-Function Plot:
  A pressure drop during the first hours of shut-in caused by tip extension or near-wellbore tortuosity.
  Shows the behavior of fracture height recession leakoff.
Rate and pressure from the Minifrac simulation for test case.
Nolte G-function plot for test case

## Slide 8
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Geomechanics Coupled Reservoir Flow Simulation
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Pressure Response Interpretation:
Bourdet Log-Log of pressure and derivative
  1/4 slope defining the before closure early time bi-linear flow.
  There is a 3/2 slope period before closure. Fracture closure is picked at the deviation from the 3/2 slope.
  A unit slope is shown after closure
  The zero slope is defined as a pseudo-radial flow regime.
Log-Log Diagnostic plot for pressure response for test case

## Slide 9
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Geomechanics Coupled Reservoir Flow Simulation
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Pressure Response Interpretation:
After-Closure Analysis
  Radial flow regime can be observed,
  Identified by a unit slope of the pressure derivative.
  The slope is used to calculate the transmissibility.
  Knowing frac height and fluid viscosity, permeability can be determined
After Closure Analysis- Square Linear Flow Time Function
After Closure Analysis Radial Flow Time Function Plot
 | Geomechanics Coupled Flow Simulation | Minifrac Field
Initial Reservoir Pressure (psi.) | 5,503.0 | 5,644.6
Closure pressure (psi.) | 8,182.9 | 6,677.6
ISIP (psi.) | 10,673.0 | 7,801.7
kh (md.ft) | 4.14 | 1.65
Permeability, (μd) | 0.08 | 0.011
 | Geomechanics Coupled Flow Simulation | Minifrac Field
Initial Reservoir Pressure (psi.) | 5,503.0 | 5,644.6
Closure pressure (psi.) | 8,182.9 | 6,677.6
ISIP (psi.) | 10,673.0 | 7,801.7
kh (md.ft) | 4.14 | 1.65
 | 0.08 | 0.011

## Slide 10
Conclusion and Next steps
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
The model, can possibly couple the fluid flow and matrix deformation in the presence of natural fractures.
The model, can possibly capture different flow regimes during falloffs.
Further investigation should be done to verify the model.
  Effect of natural fracture density on pressure response
  Effect of stress variations
  Range of permeabilities on time needed to reach closure and late time flow regimes.
  Effect of injected volume on time needed to reach late time flow regimes.
Geomechanics Coupled Reservoir Flow Simulation

## Slide 11
Geomechanics Coupled Reservoir Flow Simulation
Semi-Analytical Modeling
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 12
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Semi-Analytical Model
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Secondary Fracture
Wellbore
Hydraulic Fracture
Secondary Fracture
Wellbore
Hydraulic Fracture
Challenges with complex fractures and NF Distribution

## Slide 13
Couples three models using continuity of mass and pressure at the fracture matrix interfaces.
  Reservoir-flow model (Izadi et al. 2007)
  Fracture-flow model
  Fracture Leakoff/propagation geomechanical model
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Semi-Analytical Model
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Secondary Fracture
Wellbore
Hydraulic Fracture

## Slide 14
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Semi-Analytical Model: Reservoir-flow Model
Advisory Board Meeting, November 8, 2019, Golden, Colorado
2D diffusivity equation governs transient flow
  : source function for vertical well
  : source function for hydraulic and naturally fractures

## Slide 15
  For Hydraulic fracture:
  For Natural Fractures:
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Semi-Analytical Model: Fracture-Flow Model
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Zn = Zwhfn
qwhfn
Zn = Lfn
Zn = 0
Flow inside and around hydraulic fractures
Zn = Lfn
Zn = 0
Flow inside and around Natural fractures
Flux Distribution
  Pressure at center of jth segment of the kth fracture
= 0

## Slide 16
Fracture initiation and fluid leakoff rate
  Linear fracture propagation and rectangular cross-section
    Both are updated at each time step
  Fluid is partially stored in the fracture. Residual leaves fracture face into reservoir
  At each time step the adjusted fracture dimension is used to calculate the pressure along the fracture.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Semi-Analytical Model: Geomechanical model

## Slide 17
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Ongoing Projects
Advisory Board Meeting, November 8, 2019, Golden, Colorado
1. Cross-discipline leveraging of machine learning, and data analytics
Limit the subjectivity in the determination of minifrac parameters
By applying machine learning and artificial neural network methods
To predict (pc, tc, kh, … ). Other parameters ?
Minimize the shortcoming in determining the closure pressure for non-ideal or subjective conditions.

## Slide 18
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Ongoing Projects
Advisory Board Meeting, November 8, 2019, Golden, Colorado
2. Characterization of Frac Stage Geometry and Conductivity
Data processing
Picking the LOF period at the end of stage pumping
cleaning, smoothing and reducing points.
Log-Log Diagnostic Plot
Investigation of flow regimes
Tie LOF analysis with Tracers
and Production logs (if available)
Tie LOF analysis with Build up
Stage Properties
Fracture dimensions & conductivity.
SRV Calculations
Data Acquisition
Pressure data are recorded at surface by service company conducting Frac at little or no cost.
Makes this process Cost-effective
Mohamed, M., Ibrahim, M., Ozkan E., State of The Art In Characterization of Frac Stage Geometry and Conductivity Using Pressure Leakoff. Paper SPE-200018-MS Unconventional Resources Conference to be held 18 – 19 March 2020 in Calgary, Alberta, Canada.

## Slide 19
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Ongoing Projects
Advisory Board Meeting, November 8, 2019, Golden, Colorado
2. Characterization of Frac Stage Geometry and Conductivity
Injection History
Pressure log-log Plot and Model Match

## Slide 20
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Ongoing Projects
Advisory Board Meeting, November 8, 2019, Golden, Colorado
2. Characterization of Frac Stage Geometry and Conductivity
SRV(Buildup) = 61 acres
SRV(StagexStage) > SRV(Buildup)
Chart: Calculated SRV in Acres
 | 3.253 | 6.5657 | 2.1722 | 2.8264 | 4.1322 | 2.3474 | 2.8926 | 2.1983 | 3.3237 | 2.3815 | 0.73278 | 1.3085 | 1.2562 | 1.815 | 2.6171 | 1.1253 | 1.1096 | 3.0909 | 1.5179 | 2.3554 | 0.50248 | 2.0439 | 1.565 | 0.85055 | 2.6171 | 2.9968 | 1.3085 | 3.0882 | 1.7906 | 0.25499 | 0.38843 | 2.0661 | 2.4077 | 3.3237 | 1.6529 | 0.66116 | 1.5964 | 2.3554
SRV(Buildup) = 81 acres

## Slide 21
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Thank you
Questions?