## Slide 1: Coupled Geomechanics and Flow Simulation
Philip H. Winterfeld
Research Associate Professor
Colorado School of Mines

## Slide 2
Introduction
Geomechanics should be considered, as well as flow, when simulating processes such as CO2 sequestration, geothermal energy production, and enhanced oil and gas recovery
TOUGH2-CSM: fully coupled simulator for modeling thermal-hydrological-mechanical effects in fractured and porous media
Based on TOUGH2-MP multiphase, multiple porosity fluid and heat flow formulation
Geomechanical effects added to TOUGH2-MP: simplified Mean Stress formulation; full stress tensor formulation

## Slide 3
Geomechanical Equations
Hooke’s law for thermo-multi-poroelastic medium:
Strain tensor definition:
Static equilibrium equation:
Combine into thermo-multi-poroelastic (TMP) Navier equation ( is above summation term):

## Slide 4
Mean Stress Equation
Divergence of TMP Navier equation is Mean Stress Equation:
Trace of Hooke’s law: volumetric strain equation
Simplified geomechanical formulation: fully coupled solution for mean stress and volumetric strain along with fluid and heat flow; k and ϕ depend on effective stress ()

## Slide 5
TMP Navier equation is a vector equation, so each component and its derivatives are zero; normal and shear stresses obtained from the derivatives
Normal stress (xx-component):
Shear stress (xy-component):
Normal and Shear Stresses

## Slide 6
Finite-Difference Solution

## Slide 7
Discrete Fractures, I
EDFM method - Lee et al. (2001), Li and Lee (2008), Moinfar et
al. (2014)
Primary grid is Cartesian
Fracture – planar rectangular region
with associated aperture
Fracture plane that intersects a grid block
contributes fracture volume to it
Fracture communication: Cartesian neighbors,
volumes in both have contributions from the same fracture

## Slide 8
Discrete Fractures, II
Mass and energy conservation, and geomechanics
Grid block fracture volume - sum over fractures
Fracture flow between grid blocks and
matrix-fracture flow within grid blocks
Matrix and fracture volumes each have TOUGH2-CSM
primary variables associated with them
Mixture of single porosity (matrix) and double porosity (matrix
and fracture) grid blocks

## Slide 9: In Salah Gas Project
9
Krechba gas field at In Salah - first industrial scale on-shore CO2 storage demonstration project
Satellite-based ground-deformation monitoring measures surface uplift caused by CO2 injection
Rutqvist et al. (2010): TOUGH2-FLAC simulation
4 geological layers
Horizontal injection well in center of Injection Zone, injection for
three years
TOUGH2-CSM simulation using simplified Mean Stress model

## Slide 10: Rutqvist et al. (2010) Simulation
10

## Slide 11
Figure 6.2. Surface uplift, m, for TOUGH2-CSM In Salah CO2 injection simulation; injection well shown by thick horizontal line at origin.
TOUGH2-CSM Simulation

## Slide 12
EGS Simulation
Shi (2019) - one main wellbore with injection and production simultaneously, multilateral wells (6 arms)
1000 m cube, 500 m fractured central
cube long surrounded by rock
60 vertical fractures, 20 each 30°, 90°,
and 150° in xy-plane, from injector to
producer
200 °C at the top, scCO2 at 60 °C,
50 kg/s injected for thirty years
Stress dependent fracture permeability;
fluid and heat flow, and geomechanics

## Slide 13
Simulation Comparison

## Slide 14
Simulation Comparison, II

## Slide 15
Thank You
Any Questions?