## Slide 1
Molecular Modeling of HC Mixtures in Unconventionals
Berk Coskuner
Ph.D. Petroleum Engineering
Colorado School of Mines
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado

## Slide 2
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Objective & Outline
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Objective
Demonstrate hindrance of HC transport in nanoporous media.
Outline
Investigating the behavior of a single hydrocarbon molecule in closed pore system
  Single methane molecule
  Single heptane molecule
  Mixture of a methane molecule and a heptane molecule
Molecular Dynamics Simulation of a Membrane System
  Membrane properties
  Initial Configuration
  Details of the Simulation

## Slide 3
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Dimensions & Details of the System
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Heptane
Methane
2.2149 nm
1.62462 nm
We used Virtual Nano Lab for the molecular dynamics simulation
Simulations were run for 100,000 – 200,000 time steps
Each time step is 1 femtosecond
Simulations were run at NVT Ensemble (constant # of particles, constant volume, constant temperature)
T = 500 K
For the potential parameters, we used Tersoff_CH_2010

## Slide 4
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Purpose of the Simulations
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Observe the changes in MSD of a molecule in confined environment
Relate the diffusivity to the molecular chain length
Observe translation and retention motions of a particle (if happens)
The ultimate goal is to find a connection between the permeability constant in anomalous diffusion simulation model and diffusivity coefficient from molecular dynamics simulation

## Slide 5
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Motion of a Single Methane Particle in Nanotube
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
0-45 ps., the methane molecule is trapped in the pore, causing mean square displacements less than or equal to the square of the pore diameter (262 ).
45-85 ps, the particle is moving in the nano-tube; as a result, greater mean square displacements (484 ) observed.
Time, ps
Mean Square Displacement,
Trapped
Jumped
Trapped

## Slide 6
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Motion of a Single Heptane Particle in Nanotube
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Mean Square Displacement,
Time, ps
Trapped
In this simulation, the heptane molecule is trapped and cannot leave the pore in the left.
That’s why we do not observe a sudden jump in the mean square displacement.

## Slide 7
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Motion of a Methane & a Heptane Particle in Nanotube
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Mean Square Displacement,
Time, ps
Because the simulation gives the mean square displacement of methane and heptane together, in this example, the jump in MSD was not clearly observed.
To overcome this problem, we have started using GROMACS software, which is a free molecular dynamics simulation tool.

## Slide 8
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Kerogen Model Used in Membrane Simulation
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
To be consistent with the literature, we used a kerogen model that is already presented by Ungerer et al 2015.
MD simulation input files are online.
Input files contain the Lennard Jones Parameters, Coulomb Potential Parameters and initial configuration of molecules in Kerogen.
For this work, we chose type II-D, of which the chemical formula is: .
Ungerer et al 2015

## Slide 9
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Side and Top Views of the Initial Configuration
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
YZ
XY
The orange surface represents the kerogen membrane
The red particles represent methane molecules
The green particles represent heptane molecules
The configuration was generated using Gromacs, Packmol, VMD
100 methane and 100 heptane molecules were inserted
In the membrane, we have combination of 10 kerogen molecules presented in the previous slide.

## Slide 10
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
MD Simulation Details
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
5 nm
5 nm
The maximum pore size is 5nm which lays in the middle of the membrane. (white arrow)
Considering bonded and non bonded force fields between atoms, we will be able to see the impact of adsorption on flow.
5 nm

## Slide 11
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Purpose of the Molecular Dynamics Simulation
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Hindered transport model (Z. Zhu)
diffusional flux
advective flux
adsorption
sieving
(or more generally, chemical potential )
binary diffusion coefficient,
tortuosity
specific surface area of rock sample,
density of rock sample,
adsorption capacity of rock sample for component i,
kinetic coefficient for the exponential model
time,
maximum amount of component i held due to sieving,
kinetic coefficient for the exponential model

## Slide 12
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Purpose of the Molecular Dynamics Simulation
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado
Ziming will explain the details of the model
Our goal is to
Verify the adsorption and sieving models
Determine the following parameters of each hydrocarbon component in a mixture
  Diffusivity coefficient
  Maximum adsorption coefficient
  Maximum sieving coefficient
Delineate the impact of different conditions on the diffusivity and adsorption (i.e. temperature, pressure, etc.)

## Slide 13
Thank You
Questions?
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Nov 8, 2019, Golden, Colorado