## Slide 1
Overview of Hydrogen Sulfide Removal
Meruyert Makhatova
PhD student
Petroleum Engineering
Colorado School of Mines
Research Summary
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring Spring 2020, Golden, Colorado

## Slide 2
Very toxic and pungent gas that causes harm
to equipment by reacting with steels causing pitting and stress cracking corrosion and deposition of iron sulfide scales;
to the environment, and to humans;
It is preferable to remove H2S downhole and prevent from reaching the surface;
Required concentration of H2S < 4 ppm;
Area | H2S, %
Bearberry, Canada | 91
Big Escambia Creek, US | 21
Abu Dhabi, UAE | 0.7 - 8
Mississippi, US | 29.0 – 45.2
Saudi Arabia | 1.0 - 23
Tengiz, Kazakhstan | 17
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Motivation
Advisory Board Meeting, Spring 2020, Golden, Colorado
H2S content of sour gas worldwide (Ramachandran, 2015)

## Slide 3
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Physical characteristics of H2S
Advisory Board Meeting, Spring 2020, Golden, Colorado
Parameter | Value
Molecular weight, g/g-mol | 34.1
Kinetic diameter, pm | 360
Vapor pressure, mm Hg at 25C | 15 600
Density, g/mL at 0C, 760 mm Hg | 1.5392
Boiling point, C | -60.33
Water solubility, mg/L at 20 C | 3980
Weak acid partially dissociating into bisulfide and sulfide ions:
Obakore, 2017

## Slide 4
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Sources of H2S
Advisory Board Meeting, Spring 2020, Golden, Colorado
bacterial sulphate reduction (BSR); (at temperature from 0C up to about 60-80C )
thermochemical sulphate reduction (TSR); (at temperature of about 100 -140C and depth greater than 4000 m) (Mariott, 2015)
thermal decomposition of organic sulphur compounds; (Hoffmann, 1995 )
reaction of elemental sulphur with organic matter;
*VFA - Volatile Fatty Acids: acetic, proprionic, and butyric acids

## Slide 5
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Sources of H2S cont’d
Advisory Board Meeting, Spring 2020, Golden, Colorado
Acidizing process:
- dissolution of iron sulfide
Sea-water flood: source of sulfate ions that may be converted to H2S;
Thermal recovery:
- high temperature (from 200 C up to 350 C) induces TSR reaction;
- thermal decomposition reactions of organosulfur compound;
Hydraulic fracturing: the additives (e.g. sodium dodecyl sulfate (SDS), Mariott (2015)

## Slide 6
Non-regenerative
Solid, basic metallic compounds (iron sponge);
Oxidizing chemicals;
Aldehydes and aldehyde-related products;
Triazines - reaction products of aldehydes and amines, including;
Metal carboxylates and chelates.
Regenerative
Aqueous amines (alkanolamines)
Physical solvents - methanol and glycols follow Henry’s law for dissolution of the H2S;
Membranes - based on the principle that different gases permeate at different rates due to differences in diffusivity and solubility;
Ionic liquids - molten salts consisting of large organic cations and organic or inorganic anions
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado
Gas sweetening - removal of acid gas components from sour gas streams based upon physical or chemical absorption (to liquid) or adsorption (solid)

## Slide 7: Solid scavengers: Metal-based processes
Generally zinc- or iron-based materials
Reaction product with iron (II,III) oxide - iron pyrite (FeS2):
Trivalent iron oxidize some of the sulphide to elemental Sulphur:
Water- and oil-soluble metal chelates (carboxylate groups ) - for treating drilling fluids
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado
2

## Slide 8: Oxidizing chemicals
Oxidizing agents: water-soluble salts with oxidizing anions:
NaClO2, NaBrO3, NaNO2 (downhole squeeze injection), persalts: peroxides, perchlorates, percarbonates, and others;
Reaction product - elemental Sulphur;
Peroxide chemicals convert sulfide to sulfate (Obakore, 2017)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 9: Aldehydes
Typical aldehydes: formaldehyde, glutaraldehyde, acrolein, and glyoxal
Reaction of formaldehyde with H2S - poorly soluble in water (Kelland, 2014)
Formaldehyde is a suspected carcinogen;
Used in acid stimulation - (HMTA) forms formaldehyde in situ;
Biocides - kill sulphate-reducing bacteria;
Aldehydes do not raise the pH;
Corrosive to metals
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado
From left to right: formaldehyde, acrolein, glyoxal, glutaraldehyde

## Slide 10: Alkanolamines
Alcohol derivatives of ammonia:
Weak organic bases with pH of 10–12;
Reaction leads to a Lewis acid-base complex (Maddox, 1987)
Regeneration by applying heat
The general way of removing H2S is through transformation of the H2S to elemental sulfur – Claus process (Gary, 1984)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 11: Traizines
Reaction product of alkanolamines with formaldehyde;
Water-soluble;
Raise the pH of the produced water
H2S absorbs into the aqueous triazine solution – H2S dissociates to HS- due to alkaline pH;
React with the HS− ion;
Nitrogen-sulphur replacement stages
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado
Low solubility in water

## Slide 12: Ionic liquids
Molten salts consisting of large organic cations and organic or inorganic anions;
A variety of cation and anion combinations form ILs with great potential for H2S treatment of gas
Solubility of gases
PR EOS - fugacity in gas phase
Henry’s law – fugacity in liquid solution
Activity coefficient
Unsymmetric activity coefficient
Absorption selectivity
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Hydrogen Sulfide Scavengers
Advisory Board Meeting, Spring 2020, Golden, Colorado
Mortazavi-Manesh, 2013

## Slide 13
Theoretical model
Thermodynamic equilibrium – equality of fugacities;
The fugacity, are calculated from the PR EOS
The fugacity is calculated using Henry’s law
Henry’s constant
Harvey, 1996
- reduced temperature
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Partitioning of Hydrogen Sulfide
Advisory Board Meeting, Spring 2020, Golden, Colorado
H2S | A | B | C
 | -5.7131 | 5.3727 | 5.4227
Dissociation of H2S into
Aqueous reactions (dissolution) are fast and can be represented as chemical-equilibrium reactions
Mineral dissolution/precipitation or slow kinetics reactions with scavengers are rate-dependent reactions.

## Slide 14
The governing equations
– number of aqueous components
– the chemical equilibrium constant
– the activity of component k
– stoichiometry coefficients
– the activity product
– number of reactions between aqueous components
Activity as a function of molality
Activity coefficient (B-dot model)
- temperature dependent parameters;
– ion size parameter;
– charge of k-th ion;
– ionic strength
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Reaction Stoichiometry - Chemical Equilibrium
Advisory Board Meeting, Spring 2020, Golden, Colorado
Nghiem, 2004

## Slide 15
Rate law
– the rate
– reactive surface area
– the rate constant of mineral reaction
– chemical equilibrium constant
– activity product
– saturation index (if >1 – mineral dissolution; if <1 – mineral precipitation)
– mole number
- number of reactions between mineral and aqueous components
Porosity change:
- reference porosity without mineral reaction
Permeability reduction (Kozeny-Carman eq.)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Reaction Stoichiometry – Mineral Reactions
Advisory Board Meeting, Spring 2020, Golden, Colorado
Nghiem, 2004

## Slide 16
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Reaction Stoichiometry – Reaction Rates
Advisory Board Meeting, Spring 2020, Golden, Colorado
e.g. triazine liquid reacting with gaseous H2S (Buhaug, 2002)
for pH<10 reaction is fast
The rate of removal of hydrogen sulfide is limited by the rate of mass transfer of H2S from the gas phase to scavenger solution droplets (Fisher et al., 2003)
- mole fraction of H2S in gas phase;
- mass transfer coefficient;
– interfacial area;
– molar gas velocity
Rajagopal, 2009

## Slide 17
New non-triazine, organic acid metal complex- based H2S scavenger (OAC) ;
continuous injection through a capillary string
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Field Cases – Downhole injection
Advisory Board Meeting, Spring 2020, Golden, Colorado
H2S Scavenger Injection System (Lehrer et al, 2015)
H2S Scavenger Comparison (Lehrer et al, 2015)

## Slide 18
The downhole injection of nitrite NO2- :
- effectively remove H2S) – for the next 7 months after 36-hour treatment;
- prevent the activity of SRB due to enhancement of denitrifying bacteria (DNB) that utilize volatile fatty acids
Dissolution of precipitated iron sulfide
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Field Cases – Nitrate/Nitrite injection
Advisory Board Meeting, Spring 2020, Golden, Colorado
H2S(gas phase) and SRB in water (Sturman et al, 1999)

## Slide 19
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Overview of Experimental Procedures
Advisory Board Meeting, Spring 2020, Golden, Colorado
The test apparatus includes
- glass reaction vessel with gas: nitrogen (N2), carbon dioxide (CO2), and H2S;
- H2S analyzer;
H2S scavenger is injected through a port at the top
H2S concentration is continuously monitored.
The acid gas is swept to a NaOH scrubber;
At high pressure and high temperature test is conducted in corrosion autoclave
Sulfide Reaction Tester (Nasr-El-Din et al, 2002)
H2S Scavenger Test Apparatus (Lehrer et al, 2015)

## Slide 20
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Conclusion
Advisory Board Meeting, Spring 2020, Golden, Colorado
Source of H2S are (1) BSR, (2) TSR, (3) Thermal decomposition of organic Sulphur, and (4) reaction with elemental Sulphur;
H2S scavengers are chemical compounds and physical solvent that neutralize H2S;
Partitioning of H2S is calculated by PR EOS and Henry’s law;
Dissociation of H2S into ions is determined by activity product () and chemical equilibrium constant ;
Mineral dissolution/precipitation and slow reactions with scavengers are the rate-dependent reactions;
Nitrate/nitrite downhole injection effectively reduced H2S concentration.

## Slide 21
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Future Work
Advisory Board Meeting, Spring 2020, Golden, Colorado
Kinetic modeling study: chemical kinetic model to study reaction of H2S with scavengers;
Validate model by comparing the outputs with the data reported in the literature;
Compositional reservoir modeling coupled with kinetic model to estimate the effectiveness of downhole removal of H2S.

## Slide 22
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring 2020, Golden, Colorado
Questions?
Thank you!