## Slide 1
Ye Tian, Ozan Uzun, Yizi Shen
Hossein Kazemi, Yu-Shu Wu
https://doi.org/10.1016/j.fuel.2020.117831
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Feasibility Study of Gas Injection in Low-Perm Changqing Oilfield
Advisory Board Meeting, Spring, 2020, Golden, Colorado

## Slide 2
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring, 2020, Golden, Colorado
Outline
Introduction
Compositional modeling
Sensitivity Analysis
Conclusions

## Slide 3: Introduction
  Changqing is the largest oilfield in China, 1.15 MMBOED in 2019
  Oil prd at south<2800m, gas prd at north>2800m
  Prd est. 1971, Jurassic formation~10mD
  Now from Upper Triassic Yanchang
    Low perm ~0.1 mD
    Low pressure 0.3~0.4 psi/ft
    Fracturing is a must, but still fast decline
    Waterflood inefficient, RF is low ~10%
Source:
PetroChina
Ordos Basin
Notes: China produced 3.8 MMBOED in 2019;
Changqing oil field is a general term that represents many individual oil and gas fields across a large area in Ordos basin.
Quite a few reservoirs have a pressure coefficient of only 0.6~0.7.

## Slide 4: Stratigraphic column in the Yanchang Formation
Zeng&Li (2009) AAPG Bull.
Fine-grained sandstone
Siltstone
Mudstone
Muddy Siltstone
Siltstone
Chang 61 25–40 m
Chang 62 25–40 m
Chang 63 60–90 m
1. Green-greyish siltstones with dark grey mud intercalation.
2. Isolated from Chang 62 above and Chang 7 below.
main producing layer
Introduction

## Slide 5
Y284 Unit and its main prd interval is Chang 631, top of Chang 63
Avg kair without confining stress 0.38 mD; Avg ϕ=12.1%;
Avg Thickness=21.2 m; Avg Swi=55%;Pi=15.8 MPa; Ti=69.7°C
756 prd (perf at top)+384 w inj (perf at bottom) for better conformance
But still, waterflood RF<<10%
Introduction
Notes: Chang 63 is the 3rd sub-member of the 6th member of the upper Triassic Yanchang formation (also known as Chang 63)
The main producing interval is Chang 631, which is a continuous sand body at the top of Chang 63 with the average thickness as 21.2 m, porosity as 12.1% and initial oil saturation as 55%.

## Slide 6: Objectives
Is gas huff-n-puff feasible?
  Gas field at north Ordos Basin
  Multistage fractured well
  Successful pilots in U.S.
Compositional modeling
  Select a typical well pattern
  Fluid characterization
  Core measurement
  History match
  Sensitivity studies

## Slide 7: Reservoir fluid characterization
 | Molar fraction, % | Pc, atm | Tc, K | Acentric factor | MW, g/mol | Volume shift
CO2 | 0.12 | 72.80 | 304.20 | 0.225 | 44.01 | 0
N2 | 0.75 | 33.50 | 126.20 | 0.040 | 28.01 | 0
CH4 | 31.72 | 45.40 | 190.60 | 0.009 | 16.04 | 0
C2H6 | 8.35 | 48.20 | 305.40 | 0.098 | 30.07 | 0
C3H8 | 9.70 | 41.90 | 369.80 | 0.152 | 44.10 | 0
C4-6 | 12.82 | 29.03 | 457.53 | 0.173 | 68.58 | 0
C7-10 | 12.86 | 21.87 | 463.77 | 0.354 | 118.75 | -0.870
C11+ | 23.67 | 13.40 | 593.72 | 1.975 | 401.94 | 0.238
8-comp fluid model
CCE, separator test
Matched Pb=13.09 MPa
GOR 120.1m3/m3

## Slide 8: Core measurement
Net confining stress, psi | ϕ, % | k, 10-3 mD
788.7 | 12.30 | 2.03
1047.4 | 12.18 | 1.70
1514.7 | 12.05 | 1.34
1512.4 | 12.02 | 1.33
1106.1 | 12.10 | 1.45
857.1 | 12.16 | 1.55
Net confining stress, psi | ϕ, % | k, 10-3 mD
735.8 | 13.64 | 6.22
985.8 | 14.12 | 5.40
1472.3 | 14.16 | 4.05
1550.5 | 14.17 | 3.91
1103.7 | 14.19 | 4.28
813.2 | 14.30 | 4.69
14 cores from 2 wells
N2 under confining stress (CMS-300)
k~2 orders of magnitudes lower than labelled
Unloading curve used
Core #2
Core #1
<<0.38mD

## Slide 9: Sector model
Poor match,
e.g. BHP
1 prd+6 inj subtracted from full-field model
  Replace black oil with compositional
  Matrix k×0.01 (based on lab measurement)
  kNF=0.015 mD, ϕNF=0.001, NF spacing 0.6×0.6×3m (input tuned based on Liu, 2010; Liu et al., 2015)
  Endpoint krwo slightly tuned
Better match
Single-porosity black-oil
model by Hu (2018)

## Slide 10: Compositional effect of injectant
 | Light |  |  | Intermediate |  |  | Heavy |  | Calculated MMP, MPa
 | CO2 | N2 | CH4 | C2H6 | C3H8 | C4-6 | C7-10 | C11+ | 
Lean gas | 0% | 0% | 100% | 0% | 0% | 0% | 0% | 0% | 27.0
 | 100% |  |  | 0% |  |  | 0% |  | 
Produced gas | 0.2% | 1.3% | 55.4% | 14.3% | 15.6% | 12.5% | 0.6% | 0.0% | 14.2
 | 57.0% |  |  | 42.4% |  |  | 0.6% |  | 
Rich gas | 0% | 0% | 0% | 100% | 0% | 0% | 0% | 0% | 6.9
 | 0% |  |  | 100% |  |  | 0% |  | 
Solvent | 0% | 0% | 0% | 0% | 100% | 0% | 0% | 0% | 3.5
 | 0% |  |  | 100% |  |  | 0% |  | 
C3H8 ×2.28
C2H6 ×1.34
Prd Gas ×1.08
50-d inj; 10-d soaking; 300-d Prd; 5 cycles
CH4 ×0.89
0.6C3H8 + 0.4Prd Gas ×1.57
Inj @30MPa (fracture pressure 31 MPa)
Waterflood ×1
Waterflood×1

## Slide 11: Why is rich gas better than lean gas?
Well placement designed for waterflood with prd at top and water inj at bottom
Rich gas MMP<lean gas MMP
Lean gas achieves miscibility at front and oil bank is displaced out of SRV
Rich gas achieves miscibility at tail and oil bank flows back more effectively
CH4 injection
C3H8 injection

## Slide 12: Effect of injection pressure
Higher the pressure, higher the oil rate;
But C2H6 @ 30MPa cannot surpass C3H8 @20MPa;
C2H6 has to >25MPa to achieve improvement;

## Slide 13: Effect of injection duration
At first, longer injection time leads to higher RF
Then it reaches a plateau with 80-day injection.
10-day inj; 10-day soaking; 340-day Prd;
20-day inj; 10-day soaking; 330-day Prd;
50-day inj; 10-day soaking; 300-day Prd;
70-day inj; 10-day soaking; 280-day Prd;
80-day inj; 10-day soaking; 270-day Prd;
90-day inj; 10-day soaking; 260-day Prd;
110-day inj; 10-day soaking; 300-day Prd;
C2H6, 8 cycles

## Slide 14: Effect of soaking duration
At first, longer soaking time leads to higher RF
Then starts to decline, maximum at 7-day soaking.
80-day inj; 3-day soaking; 277-day Prd;
80-day inj; 5-day soaking; 275-day Prd;
80-day inj; 7-day soaking; 273-day Prd;
80-day inj; 8-day soaking; 272-day Prd;
80-day inj; 10-day soaking; 270-day Prd;
80-day inj; 15-day soaking; 265-day Prd;
80-day inj; 20-day soaking; 260-day Prd;
80-day inj; 25-day soaking; 255-day Prd;
80-day inj; 30-day soaking; 250-day Prd;
C2H6, 8 cycles

## Slide 15: Effect of NF spacing
Base case uses 0.6 m. We then simulate 0.3, 8, ∞ m based on the published data
Using single porosity (NF spacing=∞) leads to little improvement even with C3H8
After re-history matching, difference is minor among 0.3, 0.6, 8m NF spacing
4. Hence using published NF data, we can confirm technical feasibility of rich gas injection
Well Name | NF spacing, m
Y284 | 0.3
Y414 | 0.4
Y286 | 0.5
Y411 | 0.7
Y287 | 1.3
Y293 | 1.4
Y285 | 3.3
Y295 | 4.3
Y290 | 7.7
NF spacing from Liu (2010)

## Slide 16
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring, 2020, Golden, Colorado
Conclusions
We used a compositional framework to study gas injection feasibility in Changqing Oifield
For the first time, we confirm technical feasibility of rich gas injection in low-perm Chang 63
Such feasibility is impacted by the injectant composition and well placement design
CH4 injection has a lower RF than waterflood, due to its high MMP
Rich gas works better with current well placement as miscible bank forms at injection tail
Huff-n-puff insensitive to uncertainties in NF spacing after history-matching BHP & water cut.

## Slide 17
Thanks for your attention.
Stay safe and productive!
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring, 2020, Golden, Colorado
Ye Tian, Ph.D. candidate
For more info: yetian@mines.edu
Or read: https://doi.org/10.1016/j.fuel.2020.117831