## Slide 1
Adsorption of Hydrocarbons on a Calcite Wall by MD Simulation
Berk Coskuner, PhD. Student
CO2, CH4, C17H36 and C10H22 molecules were simulated in a calcite pore to obtain their adsorption coefficients
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring 2020, Golden, Colorado
Notes: I think calcite is better.

## Slide 2
Zhu et al. (2019) showed that long chained hydrocarbon molecules are hindered in a shale rock.
To include the hinderance effect in a simulator, T. Calisgan and Z. Zhu are developing numerical simulations that can predict adsorption and sieving behaviors of molecules in cores / reservoirs
  For this purpose, at a certain temperature, an empirical equation for adsorption is required to get the derivative of the adsorption with respect to pressure.
On the other hand, Ziming is running experiments to see the differences between CO2 and CH4 EOR applications.
  To contribute to his results, we run 2 identical hydrocarbon mixture simulations. In one of them we presented CO2 and in the other one we presented CH4 and checked the changes in the adsorptions of the H.C. on a calcite surface.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Problem Statement
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 3
We are working on the development of empirical equations for adsorption of carbon dioxide (CO2) and methane (CH4) on calcite wall, which are presented in a decane (C10) and heptadecane (C17) mixture separately.
Gromacs (a molecular dynamics simulator) is used for this purpose.
We used the high performance computers at Mines.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Scope of Research
Advisory Board Meeting, Spring 2020, Golden, Colorado
Notes: I suggest to use C10/C17 instead of DEC/HTP.

## Slide 4
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Approach
Advisory Board Meeting, Spring 2020, Golden, Colorado
CO2, C10, C17 MIXTURE
CHANGE THE NUMBER OF CO2 MOLECULES ONLY
KEEP THE MOLE FRACTIONS CONSTANT BY CHANGING THE NUMBER OF EVERY MOLECULE TYPE AT THE SAME RATIO
CH4, C10, C17 MIXTURE
CHANGE THE NUMBER OF CH4 MOLECULES ONLY
KEEP THE MOLE FRACTIONS CONSTANT BY CHANGING THE NUMBER OF EVERY MOLECULE TYPE AT THE SAME RATIO
Color Code
Completed
In progress (some results are presented)
Not started

## Slide 5
We followed the same procedure for CO2 and CH4. To keep it simple, below we only explain the procedure for CO2.
For this mixture, we run two different simulations, at first we had a constant number of C10 and C17, but changing number of CO2 to control the pressure.
In the second one, we kept the mole fraction constant and changed the number of each molecule type at a same ratio to control the pressure.
The first one tells us how does the adsorption changes with addition of CO2, whereas the second one shows how does the adsorption change with respect to the pressure only.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Approach
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 6
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Simulation Details
Advisory Board Meeting, Spring 2020, Golden, Colorado
Changing Number of CO2
Constant Mole Fraction
Mole fraction
  0.28 C10
  0.07 C17
  0.65 CO2/CH4
Number of molecules
  260 C10
  65 C17
  50 to 1100 CO2/CH4 molecules (50, 100,150, … 1050, 1100)
Temperature: 300 K
Simulated for 3000 picoseconds (3 ns)
Fluid in between two calcite sheet
In the figure, the green, red and pink molecules represent CO2, C10 and C17 respectively. The grey surfaces are the calcite walls.

## Slide 7
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Simulation Details
Advisory Board Meeting, Spring 2020, Golden, Colorado
CO2 molecules in this void space are in gas phase. To calculate the pressure of CO2, we captured it’s density in this volume and read the pressure from the density vs pressure graph of CO2.
The graph below is constructed by using the EOS.
From: nist.gov

## Slide 8
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: CO2 (Changing # of CO2)
Advisory Board Meeting, Spring 2020, Golden, Colorado
The figures represent results of 1 single simulation (at 300 K and 645 psi)
The graph shows the distribution of the density of CO2 along the simulation box (figure below) at different time steps.
One can see that as the time steps approach to 3000 ps, the density stabilizes.
To get the density of CO2 adsorbed on the CaCO3 wall at 645 psi and 300 K, we take the average of the densities on each surfaces.

## Slide 9
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: CO2 (Changing # of CO2)
Advisory Board Meeting, Spring 2020, Golden, Colorado
Running the simulation at different pressures and capturing the density data of adsorbed CO2 molecules on the CaCO3 surface, we get the following graph.
The orange dots represent the results of each MD simulation.
The blue line is the equation that we fit on the dots.
A = 950 kg/m3
B = 0.005 psi−1
Notes: Why density is in the unit of kg/m^3 not kg/m^2?
Can you add C10 on the wall and C17 on the wall as well?

## Slide 10
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: CO2 (Constant Mole Fraction)
Advisory Board Meeting, Spring 2020, Golden, Colorado
To increase the pressure, the number of molecules of each component is increased at the same ratio.
The orange dots represent the results of each MD simulation.
The blue line is the equation that we fit on the dots.
A = 830 kg/m3
B = 0.007 psi−1
Notes: Why density is in the unit of kg/m^3 not kg/m^2?
Can you add C10 on the wall and C17 on the wall as well?

## Slide 11
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: Constant vs. Variable Composition
Advisory Board Meeting, Spring 2020, Golden, Colorado
The graph compares the equations that we matched to the adsorption data from the MD simulations. The results suggest a significant difference between two approaches.
To get the derivative of adsorption with respect to pressure only, we’ll use constant composition results.
To check the results of CO2 injection experiments, we’ll use the variable compositions results, at which the number of CO2 molecules only were increased to pressurize the system, and the # of hydrocarbons were not changed.
Notes: Why density is in the unit of kg/m^3 not kg/m^2?
Can you add C10 on the wall and C17 on the wall as well?

## Slide 12
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: Constant vs. Variable Composition
Advisory Board Meeting, Spring 2020, Golden, Colorado
The graphs compare the adsorption of different types of molecules in constant composition and constant variable simulation cases.
It’s observed that in both scenarios, CO2 adsorption is significantly higher than the hydrocarbon adsorptions because of its affinity to calcite surface.
As pressure increases the hydrocarbon molecules are replaced by CO2 molecules. Hence, the number of adsorbed CO2 molecules increases, whereas the number of adsorbed hydrocarbon molecules decreases.
Notes: Why density is in the unit of kg/m^3 not kg/m^2?
Can you add C10 on the wall and C17 on the wall as well?

## Slide 13
Distance, nm
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: CO2 vs CH4
Advisory Board Meeting, Spring 2020, Golden, Colorado
The graph shows the results of two different simulations at 200 psi 300K.
1st simulation contains decane, heptadecane and methane. (Represented by solid lines)
2nd simulation contains decane heptadecane and carbon dioxide. (Represented by dashed lines)
To visualize it better, we put an illustration of the simulation box under the graph. The x axis of the simulation box is visually adjusted to make it identical to the x axis of the graph, for a better vision.
Calcite walls
Notes: Why density is in the unit of kg/m^3 not kg/m^2?
Can you add C10 on the wall and C17 on the wall as well?

## Slide 14
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Results: CO2 vs CH4
Advisory Board Meeting, Spring 2020, Golden, Colorado
Dashed blue line (1st simulation) shows the adsorption of CH4, which is replaced by CO2 in the second simulation (solid blue line).
The presence of CO2 swept the hydrocarbons from the calcite wall (See black lines) due to its high adsorption on the surface. We did not observe such a phenomenon in the 1st simulation.
Notes: Why density is in the unit of kg/m^3 not kg/m^2?
Can you add C10 on the wall and C17 on the wall as well?

## Slide 15
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Conclusion & Future Work
Advisory Board Meeting, Spring 2020, Golden, Colorado
So far:
We run MD simulations to capture the adsorption vs pressure graph of CO2, CH4, C17H36 and C10H22 .
We completed simulations of CO2 at constant mole fraction and changing mole fraction cases.
We investigated the effect of the composition and the pressure on the adsorption.
Adsorption coefficients are captured and an empirical model developed.
Effect of CO2 and CH4 on the adsorptions of other hydrocarbon molecules are compared.
Next:
We will complete the remaining simulations that are proposed in this presentation.
We are working on an MD simulation of a real oil composition used by Ziming in his experiments.

## Slide 16
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Future Work Initial Results
Advisory Board Meeting, Spring 2020, Golden, Colorado
Configuration of the Niobrara oil molecules and the calcite walls in the simulation box.
Model setup
  Niobrara pore – calcite wall, slit geometry
  Niobrara oil - simplified, 4 components
  OPLS-AA force field for hydrocarbons
  TraPPE force field for
  5 nanoseconds
  300 K
  Simulated in GROMACS 2020.1

## Slide 17
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Future Work Initial Results
Advisory Board Meeting, Spring 2020, Golden, Colorado
Observations
  CO2 molecules sweep adsorbed hydrocarbon molecules from calcite surface.
  CO2 molecules adsorb to calcite surface.
  butane molecules (representative of light hydrocarbon group) show an excess near the walls (now mostly occupied by CO2).
  support the experimental observation that CO2 is able to alleviate selective hindrance that occurred during flow of crude oil in Niobrara shale.

## Slide 18
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring 2020, Golden, Colorado
THANK YOU