## Slide 1
Estimating relative permeability from two-phase flow experiments in microfluidic micromodels
Medet Madalimov
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 2
Objectives
Introduction
Methodology
  3.1. Micromodel
  3.2. Experimental preparation and set up
  3.3. Data Analysis
Experimental Result
Conclusion and future work
References
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Table of contents
Advisory Board Meeting, Spring 2020, Golden, Colorado
Notes: Here is a content of my presentation . I will start with the Objective part, what were the aims of this work. Then move on to introduction, describing briefly theory behind conducted work. In methodology part I will present the network pattern and materials that were used to fabricate the micromodels, show experimental set up and preparation, and data analysis workflow will be presented. Afterward, will show the experimental results and end up with preliminary conclusion and future work.

## Slide 3
Conduct two phase flow displacement experiments in transparent microfluidic micromodel
Define the experimental procedure to estimate relative permeability from microfluidics experiments;
Develop procedures to obtain relative permeability from image processing
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Objectives
Advisory Board Meeting, May 30, 2020, Golden, Colorado

## Slide 4
Multiphase fluid flow in reservoir is particularly important to achieve optimum recovery. Particular interest lay on understanding of multiphase fluid flow in micron scale pore channels of the medium.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Introduction
Advisory Board Meeting, Spring 2020, Golden, Colorado
Micromodels have become popular to visualize and measure multiphase flows through porous media.
Fig.1 – Microfluidic micromodel
Notes: In this work, two phase flow experiments were conducted, oil and water. And the understanding of multiphase fluid flow in pore scale is challenging but very important to achieve optimum recovery. Meanwhile, microfluidic micromodel allow us to simulate multiphase fluid flow in pore scale, visualize and measure fluid flows though porous media.

## Slide 5
Absolute permeability – property of the rock
Effective permeability in two phase fluid flow
Multiphase flow in porous media
is governed by Darcy’s law:
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Introduction – Relative Permeability
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig. 2 - Relative permeability
(Dake, 1971)
and
Notes: Absolute permeability – property of the rock, obtained when the rock is completely saturation with single fluid.
If there are two fluids (oil and water) flowing simultaneously through porous media, then each fluid has its own effective permeability

## Slide 6
USS technique to measure relative permeability – Johnson et al (1957)
Theory assumes two conditions:
  high flow velocity;
  constant flow rate.
and
where:
- are fraction of displacing and displaced phase in flowing system;
- - relative injectivity
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Introduction – Relative permeability (Johnson et al. (1957))
Advisory Board Meeting, Spring 2020, Golden, Colorado
Notes: Johnson et al (1957) method was developed for calculating water-oil relative permeability from waterflood data (from core sample).
Theory assumes two conditions: high flow velocity (ignore capillary pressure) and constant flow rate.
Where are fraction of displacing and displaced phase in flowing system; designated as relative injectivity, defined as the ratio of the intake capacity at any given flood stage to the intake capacity of the system at the very initiation of the flood.
Johnson et al (1957) method was developed for calculating water-oil relative permeability from waterflood data (from core sample).
Theory assumes two conditions: high flow velocity (ignore capillary pressure) and constant flow rate.
Where 𝑓, 𝑓_𝑜are fraction of displacing and displaced phase in flowing system; 𝐼_𝑟 designated as relative injectivity, defined as the ratio of the intake capacity at any given flood stage to the intake capacity of the system at the very initiation of the flood.

## Slide 7
Norland Optical Adhesive 81 (NOA81)
NOA81 has properties to work as a microfluidic device material:
  Cured NOA81 is perfectly transparent
  NOA81 has better chemical resistance to organic solvents (than PDMS)
  Many surface treatments of NOA81 are available (hydrophilic or hydrophobic).
  NOA81 has high Young’s modulus (around 1GPa)
  Fabrication of NOA81 devices is simple and fast.
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Introduction – NOA81 microfluidic micromodel
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 8
Text
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Micromodel
Advisory Board Meeting, Spring 2020, Golden, Colorado
Scanned image of sandstone cross-section was used as a network design.
Pattern dimension is 1130 x 850
Channel depth is 15
Porosity – 25%
Fig. 4 - Network design. Dashed area indicates solid material
Fig. 3 – original (a) and CAD format (b) of rock cross-section pattern.

## Slide 9
Fabrication of micromodel devices is based on the technique of soft lithology
Two-layer etching was applied:
  channel depth – 15
  inlet/outlet channel – 100
Half curing method was used to transfer network design from master to NOA81 by UV-light exposure
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Micromodel
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 5. NOA81 micromodel fabrication process. (Kenzhekhanov, 2016).

## Slide 10
Water and oil were injected through a syringe (3mL) using a syringe pump.
Injection rate was kept constant over experiment (5mL/ min)
Temperature was controlled by heating stage
AmScope 600 digital camera was used to record all two-phase flow experiments
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Experimental preparation and set-up
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig. 6 - Schematic of experimental set-up

## Slide 11
Absolute permeability of NOA81 micromodel
Before test, micromodel was flooded with brine (2% KCl) to fully displace the air inside.
Calculate absolute permeability using Darcy’s Law
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Data Analysis
Advisory Board Meeting, Spring 2020, Golden, Colorado
Flow rate is measure by
where and are diameter and marked scale of the measuring tube,
Table 4.1 – Absolute permeability measurements

## Slide 12
Use MATLAB Image Processing Toolbox for image processing
image was converted to a binary image
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Data Analysis
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig. 7 – Example of data processing result.
Notes: Image processing used MATLAB Image Processing Toolbox. Water saturation was determined by refining regions in a cropped image (Figure 7 (a) and (b)), masking image in the foreground (water) and the background (“rocks and oil”) and performing background segmentation.
Then, the image was converted to a binary image (b) where “1” and “0” represent the white and black pixels, respectively.
Fig. 7 – Example of data processing result. (a) reservoir micromodel fully saturated with water (Sw = 100%) (b) binary image with Sw = 100%, (c) a frame of water-oil displacement, (d) a frame of water-oil displacement binary image, and (e) phase saturation screening. Black line indicates moment of (c) and (d).

## Slide 13
Relative Permeability from Image Processing
Volumetric rate of displaced fluid (oil):
Velocity of displaced fluid:
Superficial velocity:
Relative permeability of displaced fluid:
From water – oil displacement process, find ; from oil – water displacement, find
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Data Analysis
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 14
Relative Permeability using Johnson et al. method
Water saturation:
Saturation at the outlet of the core:
Fractional flow of oil and water: and
Effective viscosity (reciprocal relative mobility)
and
where
- volume of oil produced;
- pore volume injected relative to the entire core; subscripts;
b – refers to single phase flow (abs permeability measurement);
2 – outlet face of the porous body.
Ref. SPE-6045-PA
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Methodology – Data Analysis
Advisory Board Meeting, Spring 2020, Golden, Colorado

## Slide 15
Capture images from water-oil displacement test, Fig 11.
Calculate superficial velocity
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Experimental Results –
Relative Permeability from Image Processing
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 11 – First few seconds of the water- oil displacement test.

## Slide 16
The contact angle is 105° (Fig 12).
Water and oil saturations as a function of injected water pore volume (Fig 13)
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Experimental Results –
Relative Permeability from Image Processing
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 13 – Saturation profile along cumulate water injection converted to PV (Qi).
Water breakthrough ~ Sw = 27%
Fig 12 – Contact angle

## Slide 17
Cumulative injected volume and produced oil versus time (Fig 14)
Water and oil relative permeabilities (Fig 15).
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Experimental Results –
Relative Permeability from Image Processing
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 14 – Cumulative water injection (Wi) and cumulative produced oil (Np) vs time.
Fig 15 - Relative permeability from displacement experiment

## Slide 18
Average water saturation as a function of the injected PV of water, , and the water saturation at the outlet end of the core shows in Fig 16
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Experimental Results –
Relative Permeability using Johnson et al method
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 16 - Sw and Sw2 vs Injected PV

## Slide 19
oil flow fraction at the outlet of the core, , (Fig 17) and reciprocal relative mobility
oil and water relative permeabilities (Figure 18).
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Experimental Results –
Relative Permeability using Johnson et al method
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 17 - Fraction of oil flow at the outlet of the core
Chart: Relative Permeability
| 0.04 | 0.25821683507009652 | 0.30801415775216023 | 0.33 | 0.35239356969133695 | 0.39518320052201772 | 0.42854883040357494 | 0.45485535760188245 | 0.46537480473770598 | 0.47499999999999998 | 0.48 | 0.48499999999999999 | 0.49 | 0.49199999999999999 | 0.49299999999999999 | 0.49399999999999999
Oil | 0.94 | 0.40759 | 0.17767 | 0.071905 | 0.046256 | 0.10496 | 0.087299 | 0.064527 | 0.045872 | 0.016424 | 0.0085318 | 0.0085318 | 0.0085318 | 0.0034127 | 0.0017064 | 0.0017064
Water | 0.035373 | 0.051644 | 0.05559 | 0.046559 | 0.049276 | 0.052779 | 0.055649 | 0.06018 | 0.061394 | 0.061394 | 0.061394 | 0.062181 | 0.062444 | 0.062444 | 0.38571
Fig 18 - Relative Permeability

## Slide 20
Experimental workflow and analytical calculation procedures have been developed
Relative permeabilities (Fig 19).
Cross-over of kro and krw from both methods is the same (at Sw = 45%)
There are some differences in the results, and we will further analyze and confirm by conducting more experiments
Study the effects of oil-water viscous ratio and wettability change on relative permeability
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Conclusion and Future work
Advisory Board Meeting, Spring 2020, Golden, Colorado
Fig 19 – Relative permeability vs Sw from both method

## Slide 21
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Reference
Advisory Board Meeting, Spring 2020, Golden, Colorado
Bryant, S. and Blunt, M., 1992. Prediction of relative permeability in simple porous media. Physical Review A, 46(4), pp.2004-2011.
Buckley, S. E. and Leverett, M. C.: “Mechanism of Fluid Displacement in Sands” Thans., AIME (1942) 146, 107-116
Dake, L. P. 1983. Fundamentals of Reservoir Engineering. Elsevier, Amsterdam, 2nd Edition.
Johnson, E. F., Bossler, D. P., and Naumann, V. O., 1957. Calculation of Relative Permeability from Displacement Experiments. Trans., AIME (1959) 216, 370-372.
Jones, S. C., Roszelle, W. O., 1978. Graphical Techniques for Determining Relative Permeability From Displacement Experiments. Society of Petroleum Engineers of AIME
Julian David, O. A., 2009. Pore level Investigation of the Effect of Viscous Coupling, Displacement Flow Rates and Porous Medium Topology on Two-Phase Flow Relative Permeabilities. MS. University of Calgary.
Kenzhekhanov Sh. 2016. “Chemical EOR Process Visualization using NOA81 Micromodels”. MS. Colorado School of Mines.
Martin K. B., 2017. Multiphase flow in Permeable Media. A pore-scale perspective. Imperial College. London.