## Slide 1
Characterization of HF Geometry and Conductivity using Post-Stage-Pressure-Decay (PSPD)
Mohamed Mohamed, Colorado School of Mines
Research Summary
U R E P
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Colorado School of Mines
CSM
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 2
Minifrac
Main Frac
100-300 ft
15-20 ft
2
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Characterization of HF using Post-Stage-Pressure-Decay Minifrac vs. Main Frac Analysis

## Slide 3: Characterization of HF using Post-Stage-Pressure-Decay Minifrac vs. Main Frac Analysis
Multistage
3
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Notes: Minifrac falloff time range from 1 week to 2 weeks. Frac Treatment lasts for few minutes.

## Slide 4
Data Processing
-Picking the falloff period at the end of stage pumping
-Cleaning and smoothing data points.
Log-Log
Diagnostic Plot
Investigation of flow regimes using Bourdet plot
Tie/Validate Analysis
-Build up
-Tracers
-Production logs
Estimate Stage Properties
-Fracture dimensions
-Fracture conductivity.
-SRV calculations
Data Acquisition
-Pressure data are recorded at surface or BH at little or no cost.
-Makes this process Cost-effective
4
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Characterization of HF using Post-Stage-Pressure-Decay Workflow Overview

## Slide 5: Characterization of HF using Post-Stage-Pressure-Decay Data Acquisition and Processing
Short falloff period
Falloff after pumping of the pad
fracture dimensions
fracture conductivity and skin
Analyzable falloff period
fracture dimensions
fracture conductivity and skin
5
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Notes: Stage-by-stage basis

## Slide 6: Characterization of HF using Post-Stage-Pressure-Decay Pressure Diagnostics
  Taking advantage of Bourdet plot
    Derivative of with respect to logarithm of superposition time
  Matching Multi-Frac Horizontal Well (MFHW) analytical model
  Constraints
    Maximum  final stage ISIP
    Minimum  Pi (minifrac)
  Matching by varying
    fracture half-length
    fracture height
    skin
    fracture conductivity
6
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 7: Characterization of HF using Post-Stage-Pressure-Decay Field Case 1
Post-Stage-Pressure-Decay is recorded for 18 minutes
Log-log diagnostic plot of pressure derivative and MFHW analytical model solution
Fracture half-length (ft.) | 50
Total stage fracture half-length (ft.) | 250
Fracture height (ft.) | 57
Fracture conductivity () (mD.ft) | 141
SSRA (Acres) | 1.3
Skin | -1.69
Fracture half-length (ft.) | 50
Total stage fracture half-length (ft.) | 250
Fracture height (ft.) | 57
 | 141
SSRA (Acres) | 1.3
Skin | -1.69
Stage Analytical Model Solution Parameters
Stage stimulated reservoir area
7
7
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 8: Characterization of HF using Post-Stage-Pressure-Decay Field Case 1
Calculated Skin
Average skin -3.5
8
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 9: Characterization of HF using Post-Stage-Pressure-Decay Field Case 1
SRA(Stage x Stage) > SRA(Buildup)
The total SRA = is estimated to be around 81 acres
The SRA permeability = 0.001 md
Average hydraulic fracture half-length =288 ft.
Total stimulated reservoir area (SRA) = 61 acres
Approximately 25% shrinkage of SRA after roughly 3 weeks of production.
Pressure Build up Verification
9
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Notes: Pressure Build up Verification
  Bilinear and linear flow regimes are both detected,
    Hydraulic fracture half-length = 288 ft.
    SRA permeability = 0.001 md
  Total stimulated reservoir area (SRA)
    = 61 acres
  Approximately 25% shrinkage of SRA after 3 weeks of production.
  The fluid pressure in hydraulic fractures declines; consequently, the increased effective stress decreases the width of created hydraulic fractures held open with proppant, and the productivity of the well decreases as well.
Pressure Build up Verification
  Bilinear and linear flow regimes are both detected,
    Hydraulic fracture half-length = 288 ft.
    SRA permeability = 0.001 md
  Total stimulated reservoir area (SRA)
    𝑆𝑅𝐴=4×𝑛_𝑓×𝑥_𝑓×ℎ_𝑓 = 61 acres
  Approximately 25% shrinkage of SRA after 3 weeks of production.
  The fluid pressure in hydraulic fractures declines; consequently, the increased effective stress decreases the width of created hydraulic fractures held open with proppant, and the productivity of the well decreases as well.

## Slide 10
Characterization of HF using Post-Stage-Pressure-Decay Field Case 2
10
10
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Log-log diagnostic plot of pressure derivative and MFHW analytical model solution
Stage Analytical Model Solution Parameters
Fracture half-length (ft.) | 40
Number of Clusters | 3
Total stage fracture half-length (ft.) | 120
Fracture height (ft.) | 150
Fracture conductivity () (md.ft) | 5000
SRA (Acres) | 1.5
Skin | 0.02
Fracture half-length (ft.) | 40
 | 3
Total stage fracture half-length (ft.) | 120
 | 150
 | 5000
SRA (Acres) | 1.5
Skin | 0.02
Log-log diagnostic plot of pressure derivative and MFHW analytical model solution
Stage Analytical Model Solution Parameterse

## Slide 11: Characterization of HF using Post-Stage-Pressure-Decay Field Case 2
The total SRA = is estimated to be around 6.7 acres
Total stimulated reservoir area (SRA) = 5.4 acres
Approximately 20% shrinkage of SRA after roughly 3 weeks of production.
SRA(Stage x Stage) > SRA(Buildup)
11
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado

## Slide 12: Conclusions
Post-Stage-Pressure-Decay was used to characterize hydraulically created fractures through automated workflow to allow operators to review, revise, and implement fracture design changes in near real-time.
Post-Stage-Pressure-Decay was used to characterize created fractures
  Fracture conductivity
  Skin
SRA obtained from buildup analysis provides a reasonably good match with SSRA calculated from PSPD.
A shrinkage of 20-25% of SRA is observed after a period of production
  Indicates hydraulic fracture closures, possibly due to proppant crush or embedment.
12
12
UNCONVENTIONAL RESERVOIR ENGINEERING PROJECT
Advisory Board Meeting, November 8, 2019, Golden, Colorado
Notes: Knowing an approximate after pumping is crucial to minimize the delay in completions operations and for better planning
Knowing an approximate 𝑡_𝑐 after pumping is crucial to minimize the delay in completions operations and for better planning